## Slide 1: Patient’s flow
Patient’s entry
NOTE: Patients have already been triaged in another medical facility and are referred to the SARI treatment center.
At this point, all patients:
  receive a mask;
  wash their hands; and
  are directed to a dedicated individual booth in the waiting room.
programme

## Slide 2: Patient’s flow
2. Waiting room
The waiting room is composed of
different individual separated entrances
booths with and exits. This
facility is completely open [no doors] to allow a proper natural ventilation and is equipped with dedicated toilets.
programme

## Slide 3: Patient’s flow
3. Triage
Patients are investigated in an individual triage booth. A one (1) meter distance fence [1.2 meter high] separates patients from staff. This facility is completely open [no doors] to allow a proper natural ventilation and is equipped with dedicated toilets.
programme

## Slide 4: Patient’s flow
4. Sampling
The sampling room has four (4) individual booths with natural or hybrid ventilation.
NOTE: Not all of the patients have been tested, this is according to medical decision.
programme
Notes: .

## Slide 5
Patient’s flow
programme
1
1. Patient entry

## Slide 6: Patient’s flow
programme
Patient entry
Reception/screening
1
2

## Slide 7: Patient’s flow
programme
Patient entry
Reception/screening
Waiting room
3
1
2

## Slide 8: Patient’s flow
programme
Patient entry
Reception/screening
Waiting room
Patient toilets
4
3
1
2

## Slide 9: Patient’s flow
Patient entry
Reception/screening
Waiting room
Patient toilets
Triage
3
1
2
4
5
programme

## Slide 10: Patient’s flow
Patient entry
Reception/screening
Waiting room
Patient toilets
Triage
Sampling rooms
3
1
2
4
5
6
programme

## Slide 11: Patient’s flow
Patient entry
Reception/screening
Waiting room
Patient toilets
Triage
Sampling rooms
Ambulance entrance
3
1
2
4
5
6
7
programme

## Slide 12: Patient’s flow
Patient entry
Reception/screening
Waiting room
Patient toilets
Triage
Sampling rooms
Ambulance entrance
Donning/doffing
3
1
2
4
5
6
7
8
programme

## Slide 13: Patient’s flow
HEALTH
programme
EMERGENCIES
1
Patient entry
Reception/screening
Waiting room
Patient toilets
Triage
Sampling rooms
Ambulance entrance
Donning/doffing
Single fence
[1.2 meter high] is to
identify the centre area*
2
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
3
4
5
6
7
8
9

## Slide 14: Patient’s flow
programme
5. Short stay for mild and moderate cases
Patients are moved to the short stay ward where distances and natural ventilation assure IPC standards. Patients can wait a few hours for the laboratory results and receive health promotion sessions and treatment.

## Slide 15: Patient’s flow
programme
6. Discharge
If negative, patients can be referred to another health facility. If positive, Mild and Moderate cases can be referred to community facilities for isolation and follow-up.

## Slide 16: Patient’s flow
programme
7. Short stay ward – Observation and moderate case
The patient is moved to the observation room only in such cases where the medical department wants to keep him/her under observation for a few more hours.

## Slide 17: Patient’s flow
8. Severe case
Severe cases are moved directly to the severe case ward. Medical care will then be provided and a sample taken. This ward is composed of individual self- contained rooms with hybrid ventilation.
programme

## Slide 18: Patient’s flow
programme
8. Severe case
Severe cases are moved directly to the severe case ward. Medical care will then be provided and a sample taken. This ward is composed of individual self- contained rooms with hybrid ventilation.
If tested negative, the patient will be discharged through a dedicated discharge room.

## Slide 19: Patient’s flow
programme
9. Critical case
Critical cases are moved directly to the critical case ward. Medical care will then be provided and a sample taken. This ward is composed of individual self- contained rooms with hybrid ventilation.

## Slide 20: Patient’s flow
programme
9. Critical case
Critical cases are moved directly to the critical case ward. Medical care will then be provided and a sample taken. This ward is composed of individual self- contained rooms with hybrid ventilation.
If tested negative, the patient will be discharged through a dedicated discharge room.

## Slide 21: Patient’s flow – Worsening & improving medical condition
programme
Patient journey
Patient’s flow is not unidirectional as, according to medical conditions, patients can be moved from one ward to another.
For, instance a moderate patient’s condition can deteriorate, resulting in the person being move to the severe ward…

## Slide 22: Patient’s flow – Worsening & improving medical condition
programme
Patient journey
Patient’s flow is not unidirectional as, according to medical conditions, patients can be moved from one ward to another.
For, instance a moderate patient’s condition can deteriorate, resulting in the person being move to the severe ward… or to the critical ward.

## Slide 23: Patient’s flow – Worsening & improving medical condition
programme
Patient journey
Similarly, once medical conditions improve, a patient can be moved to another ward.
For instance, a critical patient’s condition can improve resulting in the person being move to the severe ward…

## Slide 24: Patient’s flow – Worsening & improving medical condition
programme
Patient journey
Similarly, once medical conditions improve, a patient can be moved to another ward.
For instance, a critical patient’s condition can improve resulting in the person being move to the severe ward… and to the short stay ward…

## Slide 25: Patient’s flow – Worsening & improving medical condition
programme
Patient journey
Similarly, once medical conditions improve, a patient can be moved to another ward.
For instance, a critical patient’s condition can improve resulting in the person being move to the severe ward… and to the short stay ward…to be finally discharged according to the discharge criteria.

## Slide 26: Patient’s flow / mild & moderate cases
programme

## Slide 27: Patient’s flow / mild & moderate cases
1
1. Patients [2 m distance*]
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 28: Patient’s flow / mild & moderate cases
1
2
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 29: Patient’s flow / mild & moderate cases
1
2
3
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 30: Patient’s flow / mild & moderate cases
1
2
3
4
4
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Doffing space
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 31: Patient’s flow / mild & moderate cases
1
2
3
4
4
5
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Doffing space
Shelf for PPE
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 32: Patient’s flow / mild & moderate cases
1
2
3
4
4
5
6
6
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Doffing space
Shelf for PPE
Patient entrance
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 33: Patient’s flow / mild & moderate cases
1
2
3
4
4
5
6
6
7
7
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Doffing space
Shelf for PPE
Patient entrance
Staff entrance only
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 34: Patient’s flow / mild & moderate cases
1
2
3
4
4
5
6
6
7
7
8
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Doffing space
Shelf for PPE
Patient entrance
Staff entrance only
Discharge room
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 35: Patient’s flow / mild & moderate cases
1
2
3
4
4
5
6
6
7
7
8
9
9
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Doffing space
Shelf for PPE
Patient entrance
Staff entrance only
Discharge room
Windows for natural ventilation
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme

## Slide 36: Patient’s flow / mild & moderate cases
1
2
3
4
4
5
6
6
7
7
8
9
9
10
Patients [2 m distance*]
Single fence [1.2 meter high] is to identify the centre area. Double fence with 1 meter distance can be used to help visitors to respect the spatial distance while visiting patients [not mandatory]
Working area [Staff only]
Doffing space
Shelf for PPE
Patient entrance
Staff entrance only
Discharge room
Windows for natural ventilation
Recommended spatial distance for IPC is 1 meter. However, in order to facilitate access and movement of health-care workers, 2 meters separation is advised.
programme
10. Observation.

## Slide 37: Patient’s flow / severe & critical cases
programme

## Slide 38: Patient’s flow / severe & critical cases
1
1. Individual doffing [one per room]
programme

## Slide 39: Patient’s flow / severe & critical cases
1
2
Individual doffing [one per room]
Self-contained room with individual terrace
programme

## Slide 40: Patient’s flow / severe & critical cases
1
2
3
Individual doffing [one per room]
Self-contained room with individual terrace
Individual toilet/shower
programme

## Slide 41: Patient’s flow / severe & critical cases
1
2
3
4
Individual doffing [one per room]
Self-contained room with individual terrace
Individual toilet/shower
Shelf for PPE
programme

## Slide 42: Patient’s flow / severe & critical cases
1
2
3
4
5
Individual doffing [one per room]
Self-contained room with individual terrace
Individual toilet/shower
Shelf for PPE
Working area [Staff only]
programme

## Slide 43: Patient’s flow / severe & critical cases
1
2
3
4
5
6
Individual doffing [one per room]
Self-contained room with individual terrace
Individual toilet/shower
Shelf for PPE
Working area [Staff only]
Patient entrance
programme

## Slide 44: Patient’s flow / severe & critical cases
1
2
3
4
5
6
7
Individual doffing [one per room]
Self-contained room with individual terrace
Individual toilet/shower
Shelf for PPE
Working area [Staff only]
Patient entrance
Staff entrance only
programme

## Slide 45: Patient’s flow / severe & critical cases
1
2
3
4
5
6
7
8
Individual doffing [one per room]
Self-contained room with individual terrace
Individual toilet/shower
Shelf for PPE
Working area [Staff only]
Patient entrance
Staff entrance only
Space for cleaning and disinfection of items.
programme

## Slide 46: Staff’s flow
programme
Staff entry
At this point all staff:
  receive a mask;
  wash their hands;
  check temperature;
  record presence.

## Slide 47: Staff’s flow
programme
2. Changing room
Male and female changing rooms to remove personal clothes and wear scrubs and boots [or closed shoes]. Staff toilets are nearby.

## Slide 48: Staff’s flow
programme
3. Triage
Patients are investigated in the individual triage booths. A one (1) meter distance fence [1.2 m high] separates patients form staff. The facility is completely open [no doors] to allow a proper natural ventilation.

## Slide 49: Staff’s flow
programme
4. Triage -Donning/Doffing
Staff can wear specific PPE before going to the patient at the triage.

## Slide 50: Staff’s flow
programme
5. Wards – Staff area
Each ward is equipped with a working space for staff where patients are not allowed. More information in the next chapter

## Slide 51: Staff’s flow - Entrance
programme